## Slide 1: Robot Path Planning Bug algorithms
Lecture taken from Howie Choset (CMU)
http://www.cs.cmu.edu/~motion

## Slide 2: What’s special about bugs
Many planning algorithms assume global knowledge
Bug algorithms assume only local knowledge of the environment and a global goal
Bug behaviors are simple:
  Follow a wall (right or left)
  Move in a straight line towards a goal
Bug1 and Bug2 assume essentially tactile sensing
Tangent Bug deals with finite distance sensing

## Slide 3: A few general concepts
Workspace W
  depending on the robot
  Could be infinite (open) or bounded (closed/compact)
Obstacle WOi
Free workspace Wfree = W | WOi

## Slide 4: The Bug algorithms
Known direction to goal
  Robot can measure distance d(x,y) between pts x and y
Otherwise local sensing

## Slide 5: The Bug algorithms
Reasonable world
  finitely many obstacles in any finite area
  a line will intersect an obstacle finitely many times
  Workspace is bounded

## Slide 6: Beginner strategy “Bug 0” algorithm
Notations:
  qhit and qgoal
  Hit point qi and leave point qi
  A path is a sequence of hit/leave pairs bounded by qstart and qgoal
H
L

## Slide 7: Beginner strategy “Bug 0” algorithm
To do
  Head toward goal
  Follow obstacles until you can head toward obstacle again
  Continue

## Slide 8: Bug Zapper
What map can foil Bug 0?

## Slide 9: Bug 1
Head to toward goal
If an obstacle is encountered circumnavigate it and remember how close you get to the goal
Return to that closest point by wall following and continue

## Slide 10: Bug 1 more formally

## Slide 11: Upper and lower bounds
What are the upper and lower bounds on the path length that the robot takes?
Lower bound:
Upper bound:

## Slide 12: Completeness
An algorithm is complete if, in finite time, it finds a path if such a path exists or terminates with failure if it does not .
Suppose BUG1 were incomplete:
  Therefore, there is a path from start to goal
  By assumption, it is finite length, and intersects obstacles a finite number of times.

## Slide 13: Conditions if Bug 1 fails
BUG1 does not find it
Either it terminates incorrectly, or, it spends an infinite amount of time
Suppose it never terminates:
  but each leave point is closer to the obstacle than corresponding hit point
  Each hit point is closer than the last leave point
  Thus, there are a finite number of hit/leave pairs; after exhausting them, the robot will proceed to the goal and terminate

## Slide 14: Conditions if Bug 1 fails
Suppose it terminates (incorrectly)
Then, the closest point after a hit must be a leave where it would have to move into the obstacle
But, then line from robot to goal must intersect object even number of times (Jordan curve theorem)
But then there is another intersection point on the boundary closer to object. Since we assumed there is a path, we must have crossed this pt on boundary which contradicts the definition of a leave point.

## Slide 15: Bug 2
Head toward goal on the m-line
If an obstacle is in the way, follow it until you encounter the m-line again.
Leave the obstacle and continue toward the goal

## Slide 16: Bug 2

## Slide 17: Bug 2 (slight change)
Head toward goal on the m-line
If an obstacle is in the way, follow it until you encounter the m-line again closer to the goal
Leave the obstacle and continue toward the goal

## Slide 18: The spiral

## Slide 19: Bug 2 more formally

## Slide 20: Bug 1 vs. Bug 2

## Slide 21: Bug1 vs. Bug2
BUG 1 is an exhaustive search algorithm – it looks at all choices before commiting
BUG 2 is a greedy algorithm – it takes the first thing that looks better
In many cases, BUG 2 will outperform BUG 1, but BUG 1 has a more predictable performance overall

## Slide 22: Upper and lower bounds of Bug 2
What are the upper and lower bounds on the path length that the robot takes?
Lower bound:
Upper bound:
ni is the # of s-line intersections of the ith obstacle

## Slide 23: A more realistic bug
As presented: global beacons plus contact-based wall following
The reality: we typically use some sort of range sensing device that lets us look ahead (but has finite resolution and is noisy).
Let us assume we have a range sensor

## Slide 24: Raw distance function
Saturated raw distance function:

## Slide 25: Intervals of continuity
Tangent Bug relies on finding endpoints of finite, continuous segments of ρR

## Slide 26: Motion to goal transitions Moving toward goal to ‘following obstacles’
Currently, the motion-to-goal behavior “thinks” the robot can get to the goal

## Slide 27: Motion to goal transitions
Now, it starts to see something --- what to do?
Ans: For any Oi such that d(Oi,qgoal) < d(x,qgoal),
choose the pt Oi that minimizes d(x,Oi) + d(Oi,qgoal)

## Slide 28: Minimize Heuristic Example
At x, the robot knows only what it sees and where the goal is
so moves toward O2. Note the line connecting O2 and goal pass through obstacle
so moves toward O4. Note that some thinking was involved and the line connecting O4 and goal pass through obstacle

## Slide 29: Motion to goal transitions
Ans: For any Oi such that d(Oi,qgoal) < d(x,qgoal),
choose the pt Oi that minimizes d(x,Oi) + d(Oi,qgoal)

## Slide 30: Transition from Motion-to-goal
Choose the pt Oi that minimizes d(x,Oi) + d(Oi,qgoal)
Problem: what if the distance starts to go up?
Solution: act like a BUG and follow boundary

## Slide 31: dmin and dleave
dmin is the shortest distance, observed thus far, between the sensed boundary of the obstacle and the goal
dleave is the shortest distance between any point in the currently sensed environment and the goal
Terminate boundary following behavior when dleave < dmin
Initialize with x = qstart and dleave = d(qstart,qgoal)

## Slide 32: Zero sensor range
Robot moves toward goal until it hits obstacle 1 at H1
Pretend there is an infinitely small sensor range and the Oi which minimizes the heuristic is to the right
Keep following obstacle until robot can go toward obstacle again

## Slide 33: Zero sensor range
Same situation with second obstacle
At third obstacle, the robot turned left until it could not increase heuristic
dmin is distance between M3 and goal, dleave is distance between robot and goal because sensing distance is zero

## Slide 34: Finite sensor range

## Slide 35: Infinite sensor range

## Slide 36: The Basic idea
A motion-to-goal behavior as long as way is clear or there is a visible obstacle boundary pt that decreases heuristic distance
A boundary following behavior invoked when heuristic distance increases.
A value dmin which is the shortest distance observed thus far between the sensed boundary of the obstacle and the goal

## Slide 37: The Basic idea
A value dleave which is the shortest distance between any point in the currently sensed environment and the goal
Terminate boundary following behavior when dleave < dmin

## Slide 38: Tangent Buy algorithm
Repeat a) Compute continuous range segments in view b) Move toward n ∈ {T,Oi} that minimizes h(x,n) = d(x,n) + d(n,qgoal)
until a) goal is encountered, or b) the value of h(x,n) begins to increase
2. follow boundary continuing in same direction as before repeating
a) update {Oi}, dleave and dmin
until
a) goal is reached b) a complete cycle is performed (goal is unreachable)
c) dleave < dmin
Note the same general proof reasoning as before applies, although the definition of hit and leave points is a little trickier.

## Slide 39: Implementing Tangent Buy
Basic problem: compute tangent to curve forming boundary of obstacle at any point, and drive the robot in that direction
Let D(x)=minc d(x,c) c ∈ ∪i WOi
Let G(x) = D(x) - W* ← some safe following distance
Note that ∇ G(x) points radially away from the object
Define T(x) = (∇ G(x)) the tangent direction
  in a real sensor (we’ll talk about these) this is just the tangent to the array element with lowest reading
We could just move in the direction T(x)
  open-loop control
Better is δx = μ(T(x)-λ(∇G(x))G(x))
  closed-loop control (predictor-corrector)