## Slide 1: Markov & Gaussian Localization Chapter 7

## Slide 2: Autonomous mobile robots
Vehicle model
Actuators
Sensors
Control
Localization & mapping
Localization
Path & motion planning
Perception
autonomy
Vehicle autonomy
Vehicle
Independent from environment
Independent from user

## Slide 3: Mobile robot localization
In robot localization it is given a map of the environment and its goal is to determine its position relative to this map given the perceptions of the environment & its movements.

## Slide 4: Mobile robot localization
Mobile robot localization can be seen as a transformation problem between the robot’s local coordinate frame and the global coordinate frame.
Most robot do not possess a sensor for measuring pose directly from a single scan.
It has to integrate data over time to determine its pose.
Localization problems assume that an accurate map is available.

## Slide 5: Examples of maps
Metric
Topological
Mosaic of a ceiling
Occupancy grid

## Slide 6: A taxonomy for localization
- Local
- Global
- Kidnapped
Static
Dynamic
Passive
Active
Single
Multi-robots
LOCALIZATION

## Slide 7: Local verses global localization
Here localization is characterized by the type of knowledge that is available initially & at run-time.
Three types of localization problem:
Position tracking: initial position known, localization is achieved by modeling noise in robot motion.
Global localization: initial pose is unknown. Solutions can not assume boundedness of the pose error. More difficult than position tracking.

## Slide 8: Local verses global localization
Kidnapped robot: a variant of global localization, but where the robot can get kidnapped and tele-operated to some other location during operation.
The kidnapped robot problem is more difficult than global localization, in that the robot might believe it knows where it is while it does not.
In global localization the robot knows that it does not know its location.
Testing a localization algorithm by kidnapping it measures its ability to recover from global failures.

## Slide 9: Static verses dynamic environments
Static environments: here the only variable quantity is the robot’s pose. All other objects in the environment remain the same.
Dynamic environments: here other quantities vary in time. Examples include moving people, movable furniture.
Localization is more difficult in dynamic environments.
Two approaches: (1) include dynamic objects in state. (2) filter sensor data to eliminate effect of un-modeled dynamics.

## Slide 10: Passive vs. active approaches
Passive: localization module only observes the robot operating. Robot is controlled by other means (maybe randomly)
Active: such algorithms control the robot to so as to minimize the localization error and the costs arising from moving a poorly localized robot into a hazardous place.
Active methods achieve better results than passive methods.

## Slide 11: Active vs. passive techniques

## Slide 12: Single robot vs. multi robots
Single robots: most common type, here all data is collected to a single platform.
Multi-robot localization: here robot can either work on their own or communicate with each other to better the localization of all.
In multi-robot localization, one robot’s belief can be used to bias another robot’s belief if relative pose of the robots is known.

## Slide 13: Markov Localization
Probabilistic localization algorithms are variants of the Bayes filter.
The straightforward application of the Bayes filter to the localization problem is called the Markov localization.
Requires a map m as input
The map plays a role in the measurement model
It is often incorporated in the motion model
Markov localization can be used for position tracking, global localization, and kidnapped robot problems.

## Slide 14: Markov localization
Markov localization transforms a probabilistic belief at time t-1 to a belief at time t
The initial belief, bel(x0) reflects the initial knowledge of the robot’s pose. This is different according to type of localization

## Slide 15: How bel(x0) is set
Position tracking. If the initial pose is known, bel(x0) is initialized by a point-mass distribution.
In practice the initial pose is known only to approximation. The belief is initialized by a narrow Gaussian distribution.
initial pose

## Slide 16: How to initialize for global localization
If the initial position is unknown, bel(x0) is initialized by a uniform distribution over the space of all legal poses in the map.
volume of the space of all poses within the map

## Slide 17: Illustration of Markov localization
Initial belief is uniform over all poses.
As the robot queries its sensors it notices that it is adjacent to one of the doors.
It multiplies its belief bel(x0) by p(zt | xt, m)

## Slide 18: Illustration of Markov localization
The lower density bel(x) is the result of multiplying this upper density into the uniform prior belief.
The result is multi-modal indicating that the robot could be one of three places facing a door.

## Slide 19: Illustration of Markov localization
As the robot moves right, the belief is convolved with the motion model p(xt | ut, xt-1)
The result is a shifted belief that is flattened out, as a result of the convolution.

## Slide 20: Illustration of Markov localization
In the final measurement, the Markov localization algorithm multiplies the current belief with the perceptual probability p(zt| xt)

## Slide 21: Illustration of Markov localization
Next as the robot navigates the belief moves with it, although it decreases due to the accumulated error.

## Slide 22: EKF localization
The Extended Kalman Filter (EKF) localization is a special case of Markov localization.
With EKF localization beliefs bel(xt) are represented by their mean μ and covariance Σt.
In EKF localization, the map is represented by a collection of features.
At any point in time t, the robot observes a vector of ranges and bearings to nearby features

## Slide 23: EKF localization
We will assume the identity of a feature is expressed by a set of correspondence variables cti, one for each feature vector zit

## Slide 24: EKF localization
In this first example we assume we have perfect correspondences and the doors are labeled (1, 2, and 3)
We will denote the measurement model as p(zt|xt, m, ct), where ct is either {1,2,3}.

## Slide 25: EKF localization
As the robot moves to the right, its belief is convolved with the Gaussian motion model.
The resulting belief is a shifted Gaussian of increased width.

## Slide 26: EKF localization
The upper density visualizes p(zt | xt, m, ct)
Folding this measurement probability into the robot’s belief yields the posterior shown on the bottom graph.

## Slide 27: EKF localization
As the robot moves down the corridor, the robot’s uncertainty in its position increases since the EKF continues to incorporate motion uncertainty into the robot’s belief.

## Slide 28: EKF localization (known correspondence)
predicted pose after motion
corresponding uncertainty in state space
Jacobians of the motion model

## Slide 29: Mathematical derivation
Using the motion model of (5.13):
At time t
At time t-1
time window over which motion is executed
The control input

## Slide 30: Mathematical derivation
We can also decompose this last equation into a noise-free component and a random noise component
At time t
g(ut,xt-1)

## Slide 31: Mathematical derivation
The EKF approximates g(ut,xt-1) as follows:
And Gt is the Jacobian of g with respect to ut and μt-1.

## Slide 32: Mathematical derivation
Calculating all these derivatives:

## Slide 33: Noise in control space
The Covariance matrix of the noise in control space is expressed as:
Transformation from control space to state space is done via a Jacobian Vt, which is the derivative of the motion function g with respect to the motion parameters ut and μt-1

## Slide 34: Calculating Vt

## Slide 35: EKF localization (known correspondence)
predicted pose after motion
corresponding uncertainty in state space
Jacobians of the motion model

## Slide 36: EKF localization algorithm
Assign to j the correspondence of the ith feature in the measurement vector
Calculates a predicted measurement
Jacobian of the measurement model
Kalman gain is computed for each observed feature
New pose estimate
Uncertainty of measurement
Estimate is updated
Measurement likelihood

## Slide 37: Linearized measurement model
Let us denote by j the identity of the landmark that corresponds to the i-th component in the measurement vector:

## Slide 38: Linearized measurement model
We can re-write this last equation as:

## Slide 39: Linearized measurement model
The Taylor series approximation allows us to write:

## Slide 40: Linearized measurement model
Calculating the derivatives we get lines 7-11

## Slide 41: Independence assumption
We assume that all feature measurement probabilities are independent given the pose xt and the map m:
This assumption is good in static environments
Allows inclusion of multiple features into our filter.

## Slide 42: Physical implementation

## Slide 43: Prediction step
ut=10cm/s;5o/s for 9 seconds
result: Arc leng=90cm & Rot = 45o
α1=10%;
α4=10%
α1=10%;
α4=30%
α1=30%;
α4=10%
α1=30%;
α4=30%

## Slide 44: Measurement prediction

## Slide 45: Correction step

## Slide 46: EKF-based localization

## Slide 47: EKF localization with unknown correspondences
The most simple way to deal with this is Maximum Likelihood (ML)
One first determines the most likely value of the correspondence value, then takes it for granted.
ML techniques are brittle if there are many equally likely hypotheses for the correspondence variable.

## Slide 48: How to deal with false correspondences
Select landmarks that are sufficiently unique and sufficiently far apart from each other.
Make sure that the robot’s pose uncertainty remains small.
These strategies are counter to each other. So finding the right granularity of landmarks can be somewhat of an art form.
The ML technique is of great practical importance.
In the table below the correspondence variable is chosen by minimizing a Mahalanobis distance.

## Slide 49: EKF localization (unknown correspondence)

## Slide 50: EKF localization (unknown correspondence)

## Slide 51: Multi-hypothesis tracking
The Multi Hypothesis Tracking (MHT) represents a belief by a mixture of Gaussians:
Here each component (track) is a Gaussian with mean μt,l and covariance Σt,l. The scalar Ψt,l > 0 is a mixture weight.

## Slide 52: MHT data association
Each mixture component relies on a unique sequence of data association decisions.
Therefore we write the data association for each track l as c1:t,l
We can now write:

## Slide 53: MHT
The MHT terminates each component whose relative mixture weight is smaller than a threshold:

## Slide 54: Limitations
EKF and MHT tend to work well only if the position uncertainty is small.
A uni-modal Gaussian is usually a good representation of uncertainty in tracking. It is not a good representation in global localization problems.
A narrow Gaussian reduces the danger of erroneous correspondence decisions. A single false correspondence can derail the tracker. The MHT is more robust to this problem, although it can fail if the correct correspondence is not amongst those in the GMM

## Slide 55: Limitations
The Taylor expansion is usually only good in close proximity to the linearization point.
As a rule of thumb, if the STD for the orientation is larger than ±20 degrees, linearization will make the system fail.
The Gaussian localization algorithms are inapplicable to global localization problems or the kidnapped robot problem.

## Slide 56: Important points
The design of the appropriate features for the EKF localization is an art.
On one hand we want multiple features to keep the uncertainty low.
On the other hand we want to minimize the chance that landmarks are confused with each other.
Here MHT is more robust.
As a rule of thumb, a large number of landmarks work better than small numbers.
It is however critical to apply mutual exclusion principle in data association

## Slide 57: Important points
EKF localization is unable to process negative information (absence of features).
EKF simply ignores the issue of negative information.
IN SPITE OF ALL THESE LIMITATIONS, EKF LOCALIZATION CAN BE EXCELLENT IF WE ADDRESS THE ISSUE OF CORRESPONDENCE.